| F10 Brake Upgrade Comparison: 550i/750i vs 760i vs X5M/X6M (E70/71) vs E60 M5 |
| --- |
| Part Numbers and Prices |  |  |  |  |  |  |  |
|  | 550i | Used | New | 750i |  | 760i (F01) | Used | New | X5/6M (E70) | New/ Reman. | E60 M5 | Used | New |
| Front Rotor | 34116785675 34116785676 | - | £ 272.68 | 34116785675 34116785676 | Same as 550i | 34116789543 34116789544 | - | £ 275.52 | 34116789069 34116789070 | £ 328.62 | 34112282805 34112282806 | Do not fit F10. 550/750 rotors can be used with e60 M5 calipers. |
| Front Caliper | 34116786817 34116786818 | £ 125.00 | £ 152.60 | 34116786817 34116786818 |  | 34116786827 34116786828 | £ 230.00 | £ 299.38 | 34117847241 34117847242 | £ 450.00 | 34112283161 34112283162 | £ 100.00 | £ 343.08 |
| Front Caliper Carrier | 34116786829 | £ 125.00 | £ 229.50 | 34116786829 |  | 34116786829 | £ 50.00 | £ 229.50 | - | - | 34112283171 | £ 100.00 | £ 229.50 |
| Front Pads | 34116851269 | - | £ 148.85 | 34116851269 |  | 34116794464 | - | £ 148.85 | 34116799964 | £ 157.97 | 34112284065 | £ 142.49 | £ 142.49 |
| Front Rebuild Kit | 34111163647 | £ 34.16 | £ - | 34111163647 |  | - | £ 34.16 | £ - |  |  |  |  |  |
| Rear Rotor | 34216775289 | £ 175.20 | £ 175.20 | N/A | Must use 550i rear set up | N/A | Must use 550i rear set up | Must use 550i rear set up | N/A | Must use 550i rear set up | N/A | Must use 550i rear set up | Must use 550i rear set up |
| Rear Caliper | 34216793047 34216793048 | £ 60.00 | £ 171.40 | N/A |  | N/A |  |  | N/A |  | N/A |  |  |
| Rear Caliper Carrier | 34216793053 34216793054 | £ 60.00 | £ 117.04 | N/A |  | N/A |  |  | N/A |  | N/A |  |  |
| Rear Pads | 34216775346 | £ 54.73 | £ 54.73 | N/A |  | N/A |  |  | N/A |  | N/A |  |  |
| Rear Rebuild Kit | - | £ 11.08 | £ - | - |  | - |  |  |  |  |  |  |  |
| Total |  | £ 1,066.70 | £ 1,322.00 |  |  |  | £ 1,099.54 | £ 1,471.62 |  | £ 1,297.60 |  | £ 965.10 | £ 1,506.12 |
| Note on caliper carrier: Correct front caliper carrier is marked with "929" on the actual carrier. The "928" carrier marking is for 348x36 rotors. |  |  |  |  |  |  |  |
| Note on X5M Upgrade: You will need a 4mm spacer and caliper bolts that are 4mm longer, as the rotor is offset outboard 4mm compared to 550i/750i set up. Wear Sensors: Rear (34356791962), Front (34356791958) |  |  |  |  |  |  |  |  |  |  |  |  |
| Rear Brake Hardware Part Numbers |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Caliper carrier bolts | 34106864424 | big ones |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Caliper bolts | 34116768190 | little ones |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Bleeder valve | 34116768188 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Cable bracket, left | 34216793043 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| cable bracket, right | 34216793044 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Dust boot | 34206786064 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Brake hose, rear | 34326775259 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Brake hose, front | 34326775261 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

| Weights (kg) and Dimensions (mm) |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | 530d | 550i | 750i | 760i (F01) | X5/6M (E70) | E60 M5 |
| Front Rotor | 11.6 | 348x30 | 14.7 | 374x36 | 14.7 | 374x36 | 14.7 | 374x36 | 17.23 | 395x36 | 13.36 | 374x36 |
| Front Caliper | 3.88 | - | 4.53 | - | 4.53 | - | 5.6 | - | 7.26 | - | 4.3 | - |
| Front Caliper Carrier | 2.03 | - | 2.07 | - | 2.07 | - | 2.07 | - | - | 0 | 2.36 | - |
| Total Weight- Front | 17.51 |  | 21.3 |  | 21.3 |  | 22.37 |  | 24.49 |  | 20.02 |  |
| Rear Rotor | 7.3 | 330x20 | 8.7 | 345x24 | N/A | - | N/A | - |  |  | N/A | - |
| Rear Caliper | 2.98 | - | 2.98 | - | N/A | - | N/A | - |  |  | N/A | - |
| Rear Caliper Carrier | 1.3 | - | 1.3 | - | N/A | - | N/A | - |  |  | N/A | - |
| Total Weight (kg) F+R | 29.09 |  | 34.28 |  | 34.28 |  | 35.35 |  | 37.47 |  | 33.0 |  |
|  |  | Delta | 5.19 |  | 5.19 |  | 6.26 |  | 8.38 |  | 3.91 |  |
|  |  |  | 18% |  | 18% |  | 22% |  | 29% |  | 13% |  |